## Slide 1
Flow simulation around bluff body:
k-ř RANS model
1/16
Computational Fluid Dynamics and Wind Engineering
Maccarone Giovanna s349134, Morandi Simone Domenico s336974
June 13, 2026

## Slide 2
Table of Contents
1 Initial Problem
2/16
Initial Problem
Initializing the Simulation
Results

## Slide 3: Project Overview & Objectives
3/16
1 Initial Problem
Flow Configuration:
Two-dimensional, incompressible flow past a sharp-edged square cylinder in a subcritic regime.
Physical Challenge:
Accurately predicting:
  Shear layer separation
  Flow reattachment
  Unsteady wake dynamics (vortex shedding)
Project Objective:
Compare the performance of two RANS turbulence models:
  k − ϵ RNG
  k − ω Standard

## Slide 4: Flow Configuration & Boundary Setup
4/16
1 Initial Problem
Flow Properties:
Unsteady, 2D flow past a square cylinder (reference dimension B).
Subcritical regime: Re ≈ 2.2 × 104.
Non-dimensionalized using ρ = 1 kg/m3, ν = 4.545 × 10−5 kg/(m·s), and U∞.
Boundary Conditions:
Inlet: Velocity-inlet, Turbulence Intensity = 2%, Length Scale = 0.5B.
Outlet: Dirichlet condition on pressure (prel = 0).
Upper/Lower Limits: Periodic conditions.
Cylinder Surface: Smooth edge (roughness = 0), no-slip (u = v = 0).
Initialization:
Uniform initial condition matching inlet values across the entire domain.

## Slide 5: Spatial Discretization 1 Initial Problem
5/16
Domain Partitioning:
The computational domain is divided into distinct macro-zones.
Mesh Strategy:
Outer Area (EUL Region): Mapped meshing, structured grid of quadrilateral cells.
Inner Area (ALE Region): Unstructured mesh of triangular cells.
Grid Boundary Layer: Finer layer of quadrilateral cells directly around the solid walls.

## Slide 6: Turbulence Modeling: RANS & k − ϵ RNG
6/16
1 Initial Problem
RANS Approach:
Non-scale resolving models.
Uses the Boussinesq hypothesis to estimate a ”turbulent viscosity” representing the average effect of turbulence.
The Closure Problem: Requires transport equations for turbulent kinetic energy (k) and its dissipation rate (ϵ).
Standard k − ϵ vs. RNG Variant:
STD Issue: Overestimates k near the front wall of bluff bodies.
RNG Solution: Fixes the coefficients and makes k production dependent on flow vorticity.

## Slide 7: Turbulence Modeling: The k − ω Model 1 Initial Problem
7/16
Addressing Near-Wall Errors:
In order to fix near-wall errors present in k − ϵ formulations, the k − ω model is introduced.
The k − ω Model:
Uses the specific dissipation rate (ω) instead of ϵ.
Main Advantage:
The mathematical equations do not become unstable near solid walls.
The model remains robust even when k is very small.

## Slide 8: Table of Contents 2 Initializing the Simulation
8/16
Initial Problem
Initializing the Simulation
Results

## Slide 9
Changing Turbulence Model
2 Initializing the Simulation
We need to change the turbulence model from k − ϵ RNG to k − ω standard.
Then we re-set the correct discretization scheme for k.
9/16

## Slide 10
First Simulation
2 Initializing the Simulation
The behavior of Cl confirms that flow is full developed after ∼ 5800 time steps.
10/16
Figure: Values of Cl for each time step.

## Slide 11: Simulation of one period
2 Initializing the Simulation
For a clean simulation, we perform an additional 161 steps in order to finish with Cl = 0.
Then we proceed with 363 steps, which cover a complete period.
Figure: Cl values throughout one period.

## Slide 12
Table of Contents
3 Results
Initial Problem
Initializing the Simulation
Results

## Slide 13
Retrieved Data
3 Results
After the simulation, we get the following data:
Reports
Cl Cd Cm u on x = 0 u on y = 0.5
Statistics
u, v statistics on x = 0 Cp, σ (Cp) u, v statistics on y = 0.5

## Slide 14
Contour plots
3 Results
Movie 1: Contour plot of the vorticity.
Movie 2: Contour plot of k.

## Slide 15
Comparison with DIMAT
3 Results
We can analyze and compare the data for Cp and σ (Cp).

## Slide 16
Lateral Velocity
3 Results
We can take a look at the mean velocity along y = 0.5.